Hurricane Katrina:

The Intersection of a Metropolis, Infrastructure and a Natural Hazard

Joseph Wartman, Ph.D., P.E.

Associate Professor of Civil, Architectural and Environmental Engineering

Drexel University

Hurricane Katrina was the most destructive natural disaster in United States history. The hurricane generated a storm surge that ultimately led to the failure of numerous levees in New Orleans and the surrounding metropolitan region. The ensuing floods left 80 percent of New Orleans below water for many weeks and resulted in the death of over 1,250 people.  This talk will present the findings of the U.S. National Science Foundation-supported Independent Levee Investigation Team's (ILIT) forensic analysis.  The majority of the approximate 20 breaches that occurred in the metropolitan were a result of overtopping and subsequent erosion; however, some of the most catastrophic collapses occurred as a result of stability failures that occurred before levee system reached it design capacity.  Many factors, both technical and non-technical, ultimately contributed to the disastrous performance of the levee system.  These include: (1) the extreme nature of the loading (i.e. Hurricane Katrina storm surge), (2) issues with the design, construction, operation and maintenance of the system, and finally, (3) “organizational” and institutional problems associated with the governmental and local organizations responsible for the design, construction, operation, maintenance and funding of the overall flood protection system.

Speaker Biography

Joseph Wartman is an Associate Professor of Civil, Architectural and Environmental Engineering at Drexel University in Philadelphia.  He conducts research and teaches in the areas of geohazards, geotechnical composite systems, and sustainable geotechnics.  He has been deeply involved in the investigation of the New Orleans Levee System performance in Hurricane Katrina as a member of American Society of Civil Engineers (ASCE) Levee Assessment Reconnaissance Team, the National Science Foundation (NSF)-sponsored Independent Levee Investigation Team, and currently the ASCE Inter-Institute Committee on Levees.   The author of over 50 professional articles, he is a member of the editorial board of the ASCE Journal of Geotechnical and Geoenvironmental Engineering and chairs the Geo-Institute Committee on Embankments, Dams, and Slopes.  Among Dr. Wartman's awards are the 2007 Geotechnical Engineer of the Year from the Philadelphia section of ASCE, the 2006 John J. Gallen Memorial Award for Technical Advancements from Villanova University, and a Faculty Early Career Development Award from the U.S. National Science Foundation.