IE Course EAEE E4001

WEEK 3:  ENVIRONMENTAL PERFORMANCE INDICES AND METRICS

When we want to compare the length of two sticks, we can put them against each other or use an accepted measure of length, such as a one-meter “yardstick” (literally a piece of wood that is 3 feet long). When we want to know the gas efficiency of a car, we speak of “miles per gallon”, in the U.S., or “kilometers per liter”, everywhere else. As environmental awareness has increased, it has become necessary to develop sets of measures by which we can measure the environmental performance of any industrial activity, company, nation, and of the entire globe.

The “environment” consists of the physical world (land, water, air), the biological world (animals, plants, humans), and the social world (humanity). It is obvious that trying to measure the environmental impact of every possible activity on this highly complex world is not an easy task and will take a very long time to complete it, if ever. However, a start has already been made and will be described in this section, with further examples to be presented throughout this course.

An environmental evaluation matrix

To simplify matters, let us consider an “environmental evaluation matrix”, the rows of which represent six broad “stages” of industrial activities:

- Extraction of materials(e.g., mining, oil drilling, agriculture, forestry, fishery)

- Processing of primary materials (e.g., cement and metal production, oil refining, food and wood processing)

- Primary fabricating (e.g., tube and wire, plastics, paper construction)

- Manufacturing (motors, cars, plastic and paper cups)

- Use of materials and products by public

- Recycling or disposal of used materials

The columns the “environmental evaluation matrix” will represent six broad “classes of environmental concerns” regarding the potential impacts of each class of activities:

- Human health (e.g, carcinogenic, respiratory, eye/ear, esthetic)

- Ecosystems (e.g., biodiversity, animals, fish, plants)

- Materials/energy resources (e.g., ore and fossil fuel reserves, forests)

- Solid residues (municipal or industrial solid wastes)

- Liquid emissions (inorganic and organic contaminants of fresh and ocean waters)

- Gas emissions (inorganic and organic gases and particulate matter emitted to the atmosphere)

We can now visualize constructing this 6 x 6 matrix  for one particular industrial activity, such as the production and use of a television set, that involves all six stages of  production and use (see adjacent Figure 1). Let us now assume that we have at our disposal a 0 to 10 “rating” of environmental concerns (with 10 representing “negligible” impact and 0  “maximum” impact). If we know enough about what it takes to make a television set, we can fill in the numbers in the matrix; the perfect score, from an environmental point of view, would be 360 (thirty six slots times 10). In reality, the score would be somewhere between 0 and 360 and anything that could be done to increase the overall rating (for example by decreasing the use of energy per viewing hour, or designing the set in such a way that the cathode ray tube could be recycled) would help the environment.

You may think that such ratings cannot be easy and you are right because we just started doing them and we have a long way to go. But as the ancients used to say  “getting started is one half of the whole job”.

Figure 1. “Cradle to Grave” Assessment of Environmental Impacts

#### Dimensional and dimensionless environmental metrics

As we do when we discuss the fuel efficiency of a car, it is useful to express environmental performance indices, or “environmental metrics”, as ratios of one quantity, e.g., kilograms of emissions of NOx or CO2, to another, e.g. per kwh produced. This particular measure has the dimensions of mass/energy (kg/kWh) and is called “dimensional”.  In contrast the metric “kg copper in copper product A per kg of copper mined for manufacture of product A” has the dimensions of mass/mass and, therefore, is “dimensionless”.  In your term paper, try to express, as much as possible, your results in the form of such dimensional or dimensionless ratios; you will be contributing to the nurturing of IE.

The “master environmental equation”

As discussed in class, because of the high fluidity of atmospheric air and the incessant wind motion over the surface of the Earth (e.g. of southwesterly winds over North America), long-lived gas species, such as carbon dioxide (life time in atmosphere of about 5 years), become evenly distributed over the entire troposphere, no matter where they were generated. The enormous emission of anthropogenic carbon to the atmosphere (presently 6.5 billion tons per year or about 6.5% of total pre-industrial emissions of carbon) has raised the specter of global warming and has brought all nations to the negotiating table (e.g. Rio and Kyoto conferences). So let us start by establishing some measure of the contribution of each nation to global warming. This can be done by means of the “master environmental equation” that consists of three terms:

- population

- material standard of living (Gross Domestic Product or GDP, in $) per person

- environmental impact per unit of material standard of living (reflects level of technology used in industrial activities

With respect to global warming, the last term can be expressed as “tons of carbon dioxide equivalent, CO2,equ per $ of GDP” where “CO2,equ“ sums up all carbon dioxide and all other “greenhouse gases (GHG)” that have an equivalent effect (e.g. one ton of methane, CH4, emissions are equivalent to about 21 tons of CO2). Accordingly, the master environmental equation is expressed in algebraic form as follows:

National environmental impact =

= (national population)*(GDP/capita)*(environmental impact/GDP).

The above equation shows that the three contributing factors are the size of population (e.g., China), very high material standard of living (e.g. the U.S.) and inefficient technology for fuel combustion and gas emission control (e.g. in developing nations). The “population” term can be reduced by public awareness or government action (China). The GDP/capita term represents the material standard of living. The third term is indicative of the technology used to produce materials and energy and to control emissions. Of course, this is the main subject of this course. It should be noted that the at the present time the Gross Domestic Product includes all products and services paid for in local currency- it does not include environmental costs of a particular activity.

Proposal: The “incremental master environmental equation”

Inspection of Figure 2 (Growth in Global Population by Geographic Area)  shows a good reason for developing a second form of the master environmental equation: The population of developing nations in Asia and Africa has exploded since the beginning of what we may call the “2nd industrial revolution” in the 1950’s. If this trend continues, the globe will face many severe problems (e.g. food, water and material shortages) besides global warming. Therefore, it is necessary for the developed nations to curb their use of material and energy resources and also for the developing ones to curb population growth; or for both to be prepared to pay the consequences of irresponsible behavior. To “level the playing field”, it may be useful to establish an “incremental master environmental equation” that uses the year 1950 as a time reference point and compute the change in the three contributing terms since 1950 and for projections into the future:

(t (National environmental impact) =

= (t oo[(national population)*  (GDP/capita)* (environmental impact/GDP)].

where the increment (t represents the product of the three terms at time t minus the same product in 1950. The first home exercise of the IE class will involve the calculation of the master equation and the incremental Master equation for five representative nations.

National material flows

One of the most useful metrics is the annual use of various materials per person and it is readily obtained from published census and production records that all nations, and states and provinces within a nation, keep.  For example, Table 1 shows the U.S 1991 material inputs to all industrial activities. It can be seen that the largest consumption is of fossil fuels, followed by construction minerals and agricultural products. The 1991 total material flow amounted to 20.25 tons per capita.

Table 1. 1991 inputs in the U.S.  economy (after Wernick and Ausubel 1995)

|  | million tons | Tons per capita |
| --- | --- | --- |
| Coal Crude oil Natural gas Other petroleum products | 843.2 667.1 377.6 62.8 | 3.34 2.64 1.49 0.25 |
| Total fossil fuels | 1950.7 | 7.72 |
| Crushed stone Sand and gravel | 1092.8 827.5 | 4.32 3.27 |
| Total construction minerals | 1920.3 | 7.60 |
| Salt Phosphate rock Clays Industrial sand and gravel Gypsum Nitrogen minerals Lime Sulfur Cement Soda ash All other | 40.6 39.9 38.8 24.8 22.9 16.6 16.0 13.1 11.5 6.9 17.7 | 0.16 0.16 0.15 0.10 0.09 0.07 0.06 0.05 0.05 0.03 0.07 |
| (Table 1 cont.) Total industrial minerals | 248.8 | 0.98 |
| Iron and steel Aluminum Copper All other | 99.9 5.3 2.2 4.2 | 0.40 0.02 0.01 0.02 |
| Total metals | 111.6 | 0.44 |
| Saw timber Pulpwood Fuel wood All other | 122.9 72.8 51.5 12.6 | 0.49 0.29 0.20 0.05 |
| Total forestry products | 259.8 | 1.03 |
| Grains Hay Fruit and vegetables Milk products Sugar crops Oilseeds Meat and poultry All other | 219.7 133.2 70.5 63.2 50.6 44.7 42.3 4.9 | 0.87 0.53 0.28 0.25 0.20 0.18 0.17 0.02 |
| Total agriculture | 629.1 | 2.49 |
| Total U.S. material inputs | 5120.3 | 20.25 |

It is interesting to compare the U.S. material flows with some other developed countries (Table 2), also for the year 1991:

Table 2. 1991 domestic consumption of materials in industrial countries (Fischer-Kowalski and Hutter, 1998)

| Nation | Germany | Japan | Netherlands | U.S.A. |
| --- | --- | --- | --- | --- |
| Population, millions | 80.0 | 124.0 | 22.5 | 252.8 |
| Consumption, tons/capita: Oil, coal, gas | 6.2 | 3.3 | 6.4 | 7.7 |
| Minerals and metals | 10.7 | 11.8 | 5.9 | 8.0 |
| Biomass | 2.6 | 1.5 | 10.2 | 3.0 |
| Total domestic consumption | 19.5 | 16.6 | 22.5 | 18.7 |

It can be seen that these numbers reflect not only different lifestyles of consumers (e.g., the per capita use of fossil fuels used in Japan is one half or less than of  the other countries because of their development of superior mass transport system) but also production and manufacturing strengths of each nation (e.g. compare the high per capita “consumption” of minerals and metals in Japan and Germany with Netherlands; and the high biomass consumption in Netherlands with that in Japan).

Just as Table 2 showed the input flows of materials to the U.S. economy, Table 3 shows how these materials are converted into domestic stocks, emissions and waste streams.

Table 3. 1991 material outputs of the U.S. economy (after Wernick and Ausubel 1995)

|  | million tons | Tons per capita |
| --- | --- | --- |
| Domestic stocks: Construction All other | 1677.1 203.2 | 6.63 0.80 |
| Total domestic stocks | 1880.3 | 7.44 |
| Atmospheric emissions: Carbon as CO2 Hydrogen Methane Carbon as CO NOx Volatile Organic Carbon (VOC) Sulfur as SO2 Particulate matter | 1367.0 254.6 29.1 29.0 19.4 17.6 10.4 5.5 | 5.41 1.01 0.12 0.11 0.08 0.07 0.04 0.02 |
| Total atmospheric emissions | 1734.7 | 6.85 |
| Residues and wastes: Processing wastes Coal ash Municipal/commercial waste Yard waste Food waste Water and wastewater sludge | 136.2 85.0 276.4 35.0 13.2 9.4 | 0.54 0.34 1.09 0.14 0.05 0.04 |
| Total residues and wastes | 555.2 | 2.20 |
| Total recycled materials | 243.8 | 0.96 |
| Total U.S. materials output | 4411.9 | 17.45 |

# Generation of wastes per unit of production

Wernick and Ausubel (1995) estimated the amount of wastes generated annually in the U.S. as the result of  fossil fuel and mineral production. Table 4 shows these estimates as tons per year and also as the ratio of  tons of waste per ton of material produced. It can be seen that from up to 12 tons of material must be moved aside to produce one ton of  fuel, mineral or metal production.

Table 4. Mining and mineral concentration wastes generated per unit of production

|  | Million tons of wastes | Million tons of production | tons of waste per ton produced |
| --- | --- | --- | --- |
| Coal, surface mining Coal, cleaning | 10042 84 | 843 | 12.0 |
| Oil & gas produced wastes Oil & gas drilling fluids | 3318 57.2 | 1044.7 | 3.2 |
| Ore wastes in metal mining “Tailings” from ore concentration | 755 409 | 111.6 | 10.4 |
| Ore wastes in phosphate mining “Tailings” from ore concentration | 262 108 | 39.9 | 9.3 |

Fraction of global production used by a nation

## A metric that can be of importance in trans-national discussions of emission rights, etc., is the fraction of global production of a specific material that is used by a particular nation. It should be understood that  this use encompasses both internal consumption and also export trade. Therefore, large industrial nations are  using a fraction of that is disproportionately high to their fraction of the world’s population. For example, Table 5 shows the 1990 global production of various materials and the respective amounts produced/imported and used/exported by the U.S. economy. It can be seen that the U.S., with about 4.5% of the world’s population, used from 6.5% to 31.9% of the global production of various materials.

Table 5. Fraction of global production of materials used by the U.S. economy (1990, ref.)

| Material | Global production, million tons | Use by U.S. economy, million tons | U.S. fraction, |
| --- | --- | --- | --- |
| Plastics | 78.3 | 25 | 31.9% |
| Synthetic ffiber | 13.2 | 3.9 | 29.5% |
| Aluminum | 17.8 | 5.3 | 29.8% |
| Phosphate | 15.7 | 4.4 | 28.0% |
| Copper (new metal) | 8.8 | 2.2 | 25.0% |
| Salt | 202.3 | 40.6 | 20.1% |
| Potash | 28.3 | 5.5 | 19.4% |
| Sand, gravel | 133.1 | 24.8 | 18.6% |
| Iron and steel | 593.7 | 99.9 | 16.8% |
| Nitrogen | 107.9 | 18 | 16.7% |
| Cement | 1251.1 | 81.3 | 6.5% |

Other useful metrics

Many other environmental metrics have been defined and  some are shown in Table 6.  They include the hydrogen/carbon ratio in fuel used (e.g. natural gas, CH4, generates more energy per kilogram of carbon emitted to the atmosphere than fuel oil), intensity of use of material (e.g. a ton of steel in an automobile is less efficient in people transport that one ton of steel in a train), and others.

Table 6. Some useful indices of environmental performance (after Wernick and Ausubel, 1995)

| Name | Dimensions | Higher values indicate |
| --- | --- | --- |
| Hydrogen to carbon ratio | Mass H / mass C | lower carbon emissions per unit of energy generated |
| Intensity of material use | $ of GDP/kg of material | economic usefulness of material |
| Intensity of carbon use | $of GDP/kg of carbon emitted | decarbonization of process/product |
| Fertilizer productivity | Tons produce/ton of fertilizers used | lower emissions of fertilizers to envir’t |
| Recycled material use | Mass of recycled material/ (recycled plus virgin material) | Conservation of primary materials |
| Restoration of forest resources | Mass of forest growth/forest products harvested | Global carbon balance, less ecosystem disruption |
| Dissipation index | 1- mass of materials dissipated into environment during production / mass materials produced | Efficiency of use of materials; also avoidance of contamination |

# Environmental indicators at the firm level

Figure 3 (Tyteca, 1998) illustrates the relationships of an industrial subsystem (e.g. , a plant,  company or industry) with three systems that envelop it:  The Earth (or environment) system, social and economic systems. The subsystem A draws raw materials and energy from the environment and discharges industrial residues in it; it draws labor from the social system and provides employment and a desirable (hence marketable) product; and derives capital from the economic system and provides value added in the form of the transformed raw materials.  In order to assure sustainability of the subsystem , environmental, social and economic inefficiencies must be reduced.

Let us assume that the relative effects of the parameters shown in Figure 3 can be accounted by means of weighting coefficients kR for raw materials R, kVA for value added VA, etc. Then, Tyteca (1998) proposed  that the economic indicator of  productivity efficiency (i.e., the indicator that concentrates on economic efficiency) can be represented by:

Eeconomic

## Similarly, the social indicator is defined by

Esocial

and the ecological indicator

Eecological

## The sign convention in the above definitions is that quantities that need to be maximized from an efficiency perspective have a positive sign in the numerator and a negative sign in the denominator; the opposite is true for quantities that should be minimized (e.g., wastes, energy consumption). Also, it is evident that all quantities must be expressed in the same units (at this time in dollars or other currency) and the ratio is dimensionless. Also, notice that the use of labor as an economic input should be minimized; while generating employment is a socially desirable output and should be maximized. Of course, the respective weighting coefficients would depend on various factors such as rate of unemployment in a particular area, cost of labor, etc.

You can see that although it will be difficult to determine units of measurement and coefficient values for the different parameters in the above definitions, if they are sound they can be used for comparative assessment of plants/firms engaged in the same activity, or for weighing potential alternatives to an existing industrial activity.  For such an assessment  of 48 U.S. electric utilities, look up the interesting article by Tyteca (1998).

Figure 3. Relation of an industrial subsystem to  the  economic, social, and Earth systems

Example of environmental metrics used by a forward looking company

The material presented in this section  was obtained from an IE term  paper by Lane (1998) in which he discussed some of the environmental metrics developed by United Techmologies Corp. (UTC) under their Environmental Health and Safety policy (1997). A tabulation of these metrics is shown in Lane-Table 1.  They include annual releases to air and water, releases of ozone depleting substances, fines paid to regulatory agencies, wastewater discharges, and reduction in electric energy costs. Lane-Table 2 compares hazardous waste generation in a five-year period  by UTC and two other companies, General Electric and Boeing Corp.

# Environmental Load Units

Suppose you want to design a new product. In deciding amongst different materials and possibly forms, wouldn’t it be great to have a system of measurement that allows you to quantify the environmental impacts of competitive materials? Well, the Swedish Environmental Institute in collaboration with Volvo   have developed an analytic tool called the Environmental Priority Strategies for Product Design (EPS). I t was created principally for use in automobile design but, with additional data, it can be used for any process or product.  It works like this: A group of knowledgeable persons examine each material and assign to it an environmental index, per kilogram of material used, or for surface coating applications, per square meter of surface coated by this material.  A  number of factors are considered in this evaluation. The first is the value of this material in terms of  non-renewable Earth resources. E.g., precious metals, that are very scarce in the Earth’s crust, are assigned very high values, as shown in the Raw Materials  tabulation (Table 7).  Second , the effect of emissions of certain materials in the atmosphere are considered (Table 8). Third, organic and inorganic emissions in water are also assigned their environmental index (Table 9). The basic idea is that if you know the amount of material used or emitted, which as we will find  out  soon is the first step in the Life Cycle Assessment or products and processes, you by the Environmental Load Unit of this material and you sum up the results. Amongst a number of competitive materials, or processing routes, the lowest score will represent  the best choice, from an environmental perspective. During this course, we will discuss several applications of this methodology.

PUT HERE THREE TABLES ON ENVIRONMENTAL LOAD UNITS FROM PP

References: Class notes;  Graedel and Allenby, IE,  163-72; Wernick and Ausubel, National Material Flows and the Environment, Wernick and Ausubel,  Annu. Rev. Energy Environ. 1995. 20: 463-92; Society’s Metabolism, Part II, Fischer-Kowalski and Huttler , J. Ind. Ecol. 1998, Vol.2, N0.4:107-136; J. Lane aEnvironmental Policy and Mterics at United Ttechnologies Corp., 1998, IE term paper, Columbia University; D. Tyteca, Sustainability Indicators at the Firm Level, J. Indust. Ecology 1998, Vol. 2, No. 4: 61-76; Steen and Ryding, The EPS Enviro-accounting Method  1992, Swedish Environmental Institute (IVL).